Long-term Goal
Real-time Application Representative (RAPR)
RAPR can generate and respond to real-time network traffic
Designed to emulate 'real' application behaviors in a controllable, repeatable, and measurable manner
Built around the MGEN toolkit and supports most of the traffic shaping functionality available in Mgen Version 5.0

---
mgen log file format
Real-time Application Representative (RAPR)
Network traffic logged in MGEN log file format so MGEN oriented post analysis tools (e.g. TRPR, Dazle) can be used to calculate performance statistics
20:40:06.085045 LISTEN proto>UDP port>5000
20:40:06.085653 SEND proto>UDP flow>1 seq>0 srcPort>5001 dst>192.168.1.102/5000 size>1024
20:40:06.094358 RECV proto>UDP flow>1 seq>0 src>192.168.1.102/5000 dst>192.168.1.100/5000 sent>20:42:46.870052 size>1024 gps>INVALID,999.000000,999.000000,-999 data>18:020402000000030450227B43040402000064
20:40:06.095694 SEND proto>UDP flow>2 seq>0 srcPort>5000 dst>192.168.1.102/5000 size>1024

---
Real-time Application Representative (RAPR)
RAPR Behavior is defined by
  - RAPR Input Script
  - RAPR Behavior Table
  - RAPR Run-time Interface

---
RAPR
Real-time Application Representative (RAPR)
RAPR Input Script
  - is used to schedule emulated application behavior over a time line
RAPR Behavior Table
  - defines behavior in response to network or application generated events
RAPR Run-Time Interface
  - can be used to inject and schedule additional RAPR behaviors

---
Real-time Application Representative (RAPR)
RAPR behavior is defined in the input script and behavior table by
  - Reception Events that direct rapr to listen for specific network traffic
  - Rapr Events & Global Commands that direct the application itself (e.g. load a dictionary, set global TTL values)
  - Behavior Events that are mainly responsible initiating network traffic and monitoring responses

---
Real-time Appliation Representative (RAPR)
“Behavior Events” are rather elementary. Include:
  - DECLARATIVE events that send TCP or UDP traffic to a destination address and complete
  - INTERROGATIVE events that send TCP or UDP traffic to a destination address and await a response. If a response is not received within a specified time period, the message will be resent N number of times

---
Real-time Appliation Representative (RAPR)
“Behavior Events” continued:
  - STREAM events that send UDP multicast traffic and wait for and react to responses from other nodes listening to the multicast address. Stream events are currently designed to facilitate VoIP traffic patterns and emulate “conversations”.
  - PERIODIC events are used to spawn other behavior event types at regular intervals

---
Real-time Appliation Representative (RAPR)
It is the interaction between the generated network traffic initiated by “Behavior Events” defined in an input script over a time line and a target node(s) response as defined in its “Behavior Table” that together emulate network enable application behavior

---
Real-time Appliation Representative (RAPR)
Generated traffic can be associated with a “logic id” put in the message payload
This “logic id” is used by the target node to look up any response behavior(s) associated with it in the receiving node(s) Behavior Table

---
Real-time Application Representative (RAPR)
A DICTIONARY is available to translate name-value pairs used by the application and scripts
Journalling capability coupled with offset enables system restart mid-test
All behavior is associated with the same seed value across multiple runs of the application such that any “random” behavior in the system is repeatable

---
INPUT SCRIPT
HOSTID 100
LOAD_DICTIONARY ./dictionary-demo.xml
RAPRPIPE rapr-demo
OVERWRITE_MGENLOG ./mgenApp-demo.log
OVERWRITE_RAPRLOG ./raprApp-demo.log
TXLOG
FLUSH
CHECK
0.0 LOGICTABLE_FILE ./logictable-demo.xml
0.0 STOP 3600.0 LISTEN UDP 5000
0.0 STOP 3600.0 LISTEN UDP %MULTICAST_SERVER_SRCPORT%
0.0 STOP 3600.0 JOIN 224.225.1.3
0.0 STOP 3600.0 JOIN %MULTICAST_VIDEO_STREAM_1%

---
INPUT SCRIPT
0.0 STOP 10.0 DECLARATIVE UDP SRC 6000 DST 192.168.1.102/5001 PERIODIC [1 1024]
3.0 DECLARATIVE UDP SRC 6000 DST %CMDR%/6001 PERIODIC [1 1024]
5.0 DURATION 50.0 INTERROGATIVE RETRYINTERVAL 5 NUMRETRIES 5 UDP SRC 5001 DST 192.168.1.102/5000 PERIODIC [1 1024] PAYLOAD 1 FAILURE 2
7.0 STREAM RESPPROB 0 50 BURSTPRIORITY 5 BURSTDURATION 5 BURSTCOUNT 10 BURSTDELAY 1 3 BURSTRANGE 1 3 TIMEOUTINTERVAL 5 UDP SRC 5011 DST 224.225.1.2/5000 PERIODIC [1 1024] PAYLOAD 1

---
Input Script
HOSTID 61
START HH:MM:SS
OFFSET 5
TOS 0x10
TTL 3
INTERFACE %MANET_MULTICAST_INTERFACE%
INPUT inputScript.rapr
RAPRLOG logfile.log
OVERWRITE_RAPRLOG logfile.log
MGENLOG mgenlogfile.log
OVERWRITE_MGENLOG mgenlogfile.log
TXBUFFER 8192
RXBUFFER 8192

---
Input Script
0.0 STOP 3600.0 RAPRFLOWID 1 DECLARATIVE UDP SRC 6000 DST 192.168.1.100/6001 PERIODIC [1 1024]
25.0 STOP RAPRFLOWID 1
25.0 CHANGE_STATE %STATE_VALUE%
30.0 CLEAR ALL [declarative|interrogative|join...]
30.0 INPUT ./raprScript.rapr
35.0 LOGICID 2

---
Behavior Table
XML file
Same event syntax as used by Input Script, e.g Behavior Events, RaprEvents, and Reception Events
Each entry in the table associated with a “logic id” within a state block
Multiple events can be defined for a single logic id
Dictionary translation available

---
Behavior Table
Logic ID can come from the following triggering events:
  - PAYLOAD logic id of an incoming RAPR message
  - A LOGICID rapr event command
  - From a SUCCESS, FAILURE, or TIMEOUT logic ID associated with a Behavior Event

---
Behavior Table
<RaprLogicTable>
   <state>
      <value>%NORMAL%</value>
        <logicid>
        <id>1</id>
        <entry>DECLARATIVE UDP SRC ...</entry>
        <entry>INTERROGATIVE TCP SRC ...</entry>
        </logicid>
    </state>
</RaprLogicTable>

---
Dictionary
“Namespace” can be used to differentiate common dictionary names e.g
  - %SERVER:IP% vs
  - %CLIENT:IP%
“PACKET” namespace reserved for information contained in an incoming mgen packet:
  - %PACKET:SRCIP%
  - %PACKET:SRCPORT%

---
Dictionary
“System” namespace reserved for access to random functions, e.g.
  - %SYSTEM:RANDOMI(5,10)%
  - %SYSTEM:RANDOMF(5,10,1)%
For example:
%SYSTEM:RANDOMI(5,10)% DECLARATIVE UDP SRC 5000 DST 192.168.1.102/6001 PERIODIC [1 1024] PAYLOAD 1
%SYSTEM:RANDOMI(12,15)% DURATION %SYSTEM:RANDOMI(1,8)% DECLARATIVE UDP SRC %SERVER_DATA_PORT% DST %PACKET:SRCIP/%PACKET:SRCPORT% PERIODIC [%SYSTEM:RANDOMI(1,4)% %SYSTEM:RANDOMI(800,1400)%]

---
Dictionary
%HOSTID% keyword can be embedded in dictionary names such that values unique to a specific host can be put in a common dictionary used in network wide “application”, e.g.
HOSTID 61
DECLARATIVE ... DST %%HOSTID%DBSERVER% ...
<field>61DBSERVER</field>
<value 192.168.1.103</value>
<field>62DBSERVER</field>
<value 192.168.1.104</value>

---
Dictionary
<RaprDictionary>
   <namespace>
       <label>NAMESPACENAME</label>
        <item>
        <field>FIELDNAME</field>
        <value>VALUE1</value>
        <value>VALUE2</value>
        </item>
    </namespace>
</RaprDictionary>

---
Dictionary
<field>SUBORDINATES</field>
<value>192.168.1.100</value>
<value>192.168.1.101</value>
DECLARATIVE UDP SRC 5000 DST %SUBORDINATES%/5000 PERIODIC [1 1024]
results in TWO behavior events:
DECLARATIVE UDP SRC 5000 DST 192.168.1.100...
DECLARATIVE UDP SRC 5000 DST 192.168.1.101...

---
Repeatable Behavior
Each Behavior Event has a Random Number Generator seeded with running seed value upon instantiation
Default seed (based on HOSTID) can be changed w/INITIAL_SEED directive.
Seeds are sent in all messages.
Behavior events triggered by incoming messages are seeded from message seed
Same seeds assigned to behavior events upon system restart w/offset value

---
Simple
Interrogative
5.0 INTERROGATIVE RETRYINTERVAL 5 NUMRETRIES 2 UDP SRC 5001 DST 192.168.1.102/6001 PERIODIC [1 1024] PAYLOAD 1
Behavior Table
Script
Script
Behavior Table
Script
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
Simple
Interrogative
5.0 INTERROGATIVE RETRYINTERVAL 5 NUMRETRIES 2 UDP SRC 5001 DST 192.168.1.102/6001 PERIODIC [1 1024] PAYLOAD 1
Behavior Table
Script
Script
Behavior Table
Interrogative
dst>192.168.1.102/6001 payload>1 UBI>1
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
Simple
Interrogative
Is it my UBI? NO? Lookup Logic ID 1
Behavior Table
Script
Script
Behavior Table
Interrogative
dst>192.168.1.102/6001 payload>1 UBI>1
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
logicid>
   <id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Lookup Logic ID 1
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
logicid>
   <id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Dest
Source
Dictionary
Log File
LogFile
Dictionary
<namespace>
   <label>DEFAULT</label>
      <field>MGEN-PATTERN</field>
      <value>PERIODIC [1 1024]</value>
      <field>SEND_FILE</field>
      <value>2</value>
    </label>

---
logicid>
   <id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
<
Dictionary
Log File
Log File
Dictionary

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
X
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
<
Dictionary
Log File
Log File
Dictionary

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
dst>192.168.1.102/6001 payload>1 UBI>1
Dest
Source
Dictionary
Log File
Log File
Dictionary
Wait 5 seconds.
Response received? No.
Send another packet

---
Simple
Interrogative
Is it my UBI? NO? Lookup Logic ID 1
Behavior Table
Script
Script
Behavior Table
Interrogative
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
logicid>
   <id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Lookup Logic ID 1
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
logicid>
   <id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Dest
Source
Dictionary
Log File
LogFile
Dictionary
<namespace>
   <label>DEFAULT</label>
      <field>MGEN-PATTERN</field>
      <value>PERIODIC [1 1024]</value>
      <field>SEND_FILE</field>
      <value>2</value>
    </label>

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Declarative
Interrogative
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
<
Dictionary
Log File
Log File
Dictionary

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Interrogative
Is it my UBI? Yes? Find interrogative object and succeed.
Dest
Source
Log success in RAPR log file
Dictionary
Log File
Log File
Dictionary

---
<ogicid>
   <id>2</id>
      <entry>DECLARATIVE TCP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %FILE-PATTERN% </entry>
 </logicid>
Behavior Table
Script
Script
Behavior Table
Was there a payload ID? Yes? Get response behavior.
Dest
Source
Dictionary
Log File
Log File
Dictionary
<name>FILE-PATTERN></name>
<value>PERIODIC [1 1048576]</value>

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Declarative
Dest
Source
dst>192.168.1.102/6001 payload>1 UBI>2
Dictionary
Log File
Log File
Dictionary
dst>192.168.1.102/6001 payload>1 UBI>2

---
Simple
Interrogative
Behavior Table
Script
Script
Behavior Table
Dest
Source
Dictionary
Log File
LogFile
Dictionary

---
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
dst>192.168.1.102/6001 payload>1 UBI>1
Dest
Source
Dictionary
Log File
Log File
Dictionary

---
<state>0,%EVENT_NOT_QUEUED%</state>
<Logicid>
<id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
   <entry>%SYSTEM:RANDOMI(5,8) DECLARATIVE TCP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
   <entry>CHANGE_UBI_STATE %PACKET:UBI% %EVENT_QUEUED%
 </logicid>
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Dest
Source
Dictionary
Log File
LogFile
Dictionary
<namespace>
   <label>DEFAULT</label>
      <field>MGEN-PATTERN</field>
      <value>PERIODIC [1 1024]</value>
      <field>SEND_FILE</field>
      <value>2</value>
    </label>

---
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
start>5.0
Declarative
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
<
Dictionary
Log File
Log File
Dictionary

---
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
start>5.0
X
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
<
Dictionary
Log File
Log File
Dictionary

---
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
start>8.0
dst>192.168.1.102/6001 payload>1 UBI>1
Dest
Source
Dictionary
Log File
Log File
Dictionary
Wait 5 seconds.
Response received? No.
Send another packet

---
<state>0,%EVENT_QUEUED%</state>
<Logicid>
<id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
start>8.0
Dest
Source
Dictionary
Log File
LogFile
Dictionary
<namespace>
   <label>DEFAULT</label>
      <field>MGEN-PATTERN</field>
      <value>PERIODIC [1 1024]</value>
      <field>SEND_FILE</field>
      <value>2</value>
    </label>

---
<state>0,%EVENT_QUEUED%</state>
<Logicid>
<id>1</id>
      <entry>DECLARATIVE UDP 5001 DST %PACKET:SRCIP%/%PACKET:SRCPORT% %MGEN-PATTERN% PAYLOAD %SEND_FILE%</entry>
 </logicid>
UBI State
Behavior Table
Script
Script
Behavior Table
Interrogative
Declarative
start>8.0
Declarative
dst>192.168.1.100/5001 UBI>1 payload>2
Dest
Source
Dictionary
Log File
LogFile
Dictionary
<namespace>
   <label>DEFAULT</label>
      <field>MGEN-PATTERN</field>
      <value>PERIODIC [1 1024]</value>
      <field>SEND_FILE</field>
      <value>2</value>
    </label>

---
UBI State
Behavior Table
Script
Script
Behavior Table
Declarative
start>8.0
Dest
Source
< dst>192.168.1.100/5001 UBI>2
< dst>192.168.1.100/5001 UBI>2
< dst>192.168.1.100/5001 UBI>2
Dictionary
Log File
LogFile
Dictionary

---
UBI State
Behavior Table
Script
Script
Behavior Table
Dest
Source
Dictionary
Log File
LogFile
Dictionary

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
INPUT SCRIPT
STREAM RESPPROB 0 25 BURSTCOUNT 5 BURSTDELAY 0 3 BURSTRANGE 5 10 UDP SRC 5001 DST 224.225.1.2/5000 PERIODIC [25 100] PAYLOAD 1
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
INPUT SCRIPT
STREAM RESPPROB 0 25 BURSTCOUNT 5 BURSTDELAY 0 3 BURSTRANGE 5 10 UDP SRC 5001 DST 224.225.1.2/5000 PERIODIC [25 100] PAYLOAD 1
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
MgenMsg dst>224.225.1.2/5000 raprPayload: payload>1 burstCount>5 seed>234872 burstDuration>8.5 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream Object w/streamId 1? No.
Lookup payload logic id in behavior table
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
 Behavior Table
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
STREAM RESPPROB %%HOSTID%PROB% BURSTDELAY 3 5 BURSTRANGE 4 10 UDP SRC 5000 DST 224.225.1.2/5000 %CHAT_PATTERN%
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
 Behavior Table
 Behavior Table

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
Instantiate new Stream objects
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
?
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Probability 0-25
Probability 26-50
84 My turn to reply?
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Probability 51-75
Probability 76-100

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Probability 0-25
Probability 26-50
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
?
Stream
 Object
    id>1
Stream
 Object
    id>1
Probability 51-75
Probability 76-100
Yes - Draw 84

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
?
NODE 1
NODE 2
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Probability 0-25
Probability 26-50
32 My turn to reply?
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Stream
 Object
    id>1
Probability 51-75
Probability 76-100

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
?
Stream
 Object
    id>1
Stream
 Object
    id>1
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3

---
VoIP
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
MgenMsg dst>224.225.1.3/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>2 burstPriority>5
Listen 224.225.1.2/5000
NODE 4
NODE 3
NODE 5

---
VoIP
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
X
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
MgenMsg dst>224.225.1.3/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>2 burstPriority>5
Listen 224.225.1.2/5000
NODE 4
NODE 3
NODE 5

---
VoIP
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
streamId>2
X
MgenMsg dst>224.225.1.2/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>1 burstPriority>0
Listen 224.225.1.2/5000
MgenMsg dst>224.225.1.3/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>2 burstPriority>5
Listen 224.225.1.2/5000
NODE 4
NODE 3
NODE 5

---
VoIP
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
streamId>2
Listen 224.225.1.2/5000
MgenMsg dst>224.225.1.3/5000 raprPayload: burstCount>4 seed>newSeed burstDuration>7 streamId>2 burstPriority>5
Listen 224.225.1.2/5000
NODE 4
NODE 3
NODE 5

---
VoIP
VoIP
VoIP
VoIP with Priority
Listen 224.225.1.3/5000
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 1
NODE 2
streamId>1
streamId>2
MgenMsg dst>224.225.1.3/5000 raprPayload: burstCount>3 seed>newSeed burstDuration>7 streamId>2 burstPriority>5
Listen 224.225.1.2/5000
Listen 224.225.1.2/5000
NODE 4
NODE 3
NODE 5

---
Fielded Applications
Situational Awareness
Logistics
Intel
VoIP
Video

---
Intel Example
Client
Server
1
1
Periodic Interrogative
Change UBI State – Event Queued
Send ACK (100 byte packet)
Wait 2-8 seconds, send URI (5 1000 byte packets)
ack
3
Change UBI State – Event Queued
Wait 3-6 seconds, send Interogative File Request (1 500-100 byte packet)
4
Change UBI State – Event Queued
Send ACK (100 byte packet)
For 75-150 seconds, send 10 1300 byte pkts
Send Variable File size
<entry>0.0 DURATION %SYSTEM:RANDOMI(1,4)% DECLARATIVE UDP SRC %SERVER:SEND_DATA_PORT% DST %PACKET:SRCIP%/%CLIENT:LISTEN_DATA_PORT% PERIODIC [%SYSTEM:RANDOMI(2,4)% %SYSTEM:RANDOMI(800,1400)%] </entry>
        <entry>%SYSTEM:RANDOMI(2,5)% DURATION %SYSTEM:RANDOMI(1,8)% DECLARATIVE UDP SRC %SERVER:SEND_DATA_PORT% DST %PACKET:SRCIP%/%CLIENT:LISTEN_DATA_PORT% PERIODIC [%SYSTEM:RANDOMI(1,4)% %SYSTEM:RANDOMI(800,1400)%] </entry>
        <entry>%SYSTEM:RANDOMI(12,15)% DURATION %SYSTEM:RANDOMI(1,4)% DECLARATIVE UDP SRC %SERVER:SEND_DATA_PORT% DST %PACKET:SRCIP%/%CLIENT:LISTEN_DATA_PORT% PERIODIC [%SYSTEM:RANDOMI(1,4)% %SYSTEM:RANDOMI(800,1400)%] </entry>
        <entry>%SYSTEM:RANDOMI(13,19)% DURATION %SYSTEM:RANDOMI(1,4)% DECLARATIVE UDP SRC %SERVER:SEND_DATA_PORT% DST %PACKET:SRCIP%/%CLIENT:LISTEN_DATA_PORT% PERIODIC [%SYSTEM:RANDOMI(1,4)% %SYSTEM:RANDOMI(800,1400)%] </entry>
ack

---
Intel Example

---
Data Anaylzer (DAZLE2)
Measures and analyzes flow information
Measures and analyzes arbitrary events
Based on RAPR log files and mod of PCAP lib
  - Aggregate data over the interface
Able to do comparisons (Go/No-Go)
  - Baseline vs performer

---
Data Anaylzer (DAZLE2)
Distinct transmission flows defined by unique flowid,source ip address/port destination address/port
For each flow consolidates data into time windows
Also consolidates “group flows” e.g. All incoming traffic to each node,

---
Data Anaylzer (DAZLE2)
Statistics include:
  - Total byte rate
  - Useful byte rate
  - Late byte rate
  - Lost byte rate
  - Overhead byte rate

---
All flows, all sources
Intel application

---
All flows, all sources
SA Application

---
DAZLE Diagram
Data Store (DB/files)
Sampling Statistics Library
RAPR Logs
File Reader Library
Event Flow Library
Filtering Library
pcap logger
Arbitrary Events
Statistics Tools Library
Viz. Library
DAZLE GUI

---
DAZLE

---
DAZLE